## Slide 1: Precise Positioning and Scanning for Microwave Imaging

## Slide 2: Breast Cancer
In Sweden More than 60 000 people per year get a cancer diagnosis.
Over 7500 are breast cancer.
20 Women get breast cancer per day.
30% of all cancer types for women is breast cancer.
The most common cancer among women.
Source: Bröstcancer – symtom, orsaker och behandling | Cancerfonden

## Slide 3: Breast cancer screening
X-ray mammography
The most common primary method
Uncomfortable breast compression
Ionizing radiation
Low contrast between glandular and tumor tissue
Low sensitivity -> Radiologist Experience.
Microwave Imaging
Noninvasive
Nonionizing radiation
Higher contrast relation for different tissues
Require a precise positioning of the sender and receiver

## Slide 4: System Description Summary – Microwave imaging
A transmitting applicator sends an electromagnetic wave to illuminate the breast.
Induced current inside the breast generates a scattered field.
A receiving applicator measures the scattered field to retrieve the electromagnetic properties of the breast.
High contrast in the electromagnetic properties between glandular and tumor tissues.

## Slide 5: Microwave imaging for breast cancer screening.
No clinical-ready system for hospital usage.
Clinical prototypes for active microwave imaging
  Require that the breast is submerged in a liquid tank.
A research group at MDU has developed a new pair of antennas that does not require the liquid tank.
The Microwave imaging require a precise position of the antennas to get good results.

## Slide 6: Project Description
The main goal is to automize the microwave measurement procedure.
  Develop a robotic system that can place the sender and receiver units around the breast and run an automated measurement sequence.
  The distance between the antenna and the breast surface should be controllable.
  The angle of incidence should be adjustable.
  The system should be able to scan non-symmetrical breast phantoms.
  A graphical user interface (GUI) is required to control the system.

## Slide 7: Focus this year
The transmitter moves only in one dimension.
The receiver moves in all the required degrees of freedom.
Build a complete system.
Prioritize the precise position of the antenna.
Investigate the data acquisition time.

## Slide 8: The system overview

## Slide 9: Receiver arm Yumi

## Slide 10: Sender arm

## Slide 11: Sensor

## Slide 12: End-effector

## Slide 13: Reference model

## Slide 14: System presentation video

## Slide 15: How it works ( software ) …