## Slide 1: Precise Positioning and Scanning for Microwave Imaging

## Slide 2: Breast Cancer
In Sweden More than 60 000 people per year get a cancer diagnosis.
Over 7500 are breast cancer.
20 Women get breast cancer per day.
30% of all cancer types for women is breast cancer.
The most common cancer among women.
Source: Bröstcancer – symtom, orsaker och behandling | Cancerfonden

## Slide 3: Breast cancer screening
X-ray mammography
The most common primary method
Uncomfortable breast compression
Ionizing radiation
Low contrast between glandular and tumor tissue
Low sensitivity -> Radiologist Experience.
Microwave Imaging
Noninvasive
Nonionizing radiation
Higher contrast relation for different tissues
Require a precise positioning of the sender and receiver

## Slide 4: System Description Summary – Microwave imaging
A transmitting applicator sends an electromagnetic wave to illuminate the breast.
Induced current inside the breast generates a scattered field.
A receiving applicator measures the scattered field to retrieve the electromagnetic properties of the breast.
High contrast in the electromagnetic properties between glandular and tumor tissues.

## Slide 5: Microwave imaging for breast cancer screening.
No clinical-ready system for hospital usage.
Clinical prototypes for active microwave imaging
  Require that the breast is submerged in a liquid tank.
A research group at MDU has developed a new pair of antennas that does not require the liquid tank.
The Microwave imaging require a precise position of the antennas to get good results.

## Slide 6: Project Description
The main goal is to automize the microwave measurement procedure.
  Develop a robotic system that can place the sender and receiver units around the breast and run an automated measurement sequence.
  The distance between the antenna and the breast surface should be controllable.
  The angle of incidence should be adjustable.
  The system should be able to scan non-symmetrical breast phantoms.
  A graphical user interface (GUI) is required to control the system.

## Slide 7: Focus this year
The transmitter moves only in one dimension.
The receiver moves in all the required degrees of freedom.
Build a complete system.
Prioritize the precise position of the antenna.
Investigate the data acquisition time.

## Slide 8: The system overview
The Breast is scanned using a laser sensor to create a point cloud from the breast surface.
Using a surface reconstruction algorithm, we can reconstruct a mesh surface from the point cloud.
Using the GUI the user can choose a scanning point or scanning area with a specified number of points in the Area.

## Slide 9: Receiver arm Yumi

## Slide 10: Sender arm

## Slide 11: Sensor

## Slide 12: End-effector

## Slide 13: Reference model

## Slide 14: System presentation video

## Slide 15: How to scan and reconstruct a surface
Choice of the Scanning device and scanning algorithms
Surface preknowledge
  Smooth
  Convex

## Slide 16: How to scan and reconstruct a surface
Reconstruction algorithms
  Power crust
  Alfa shape
Algorithm requirements
  Points density

## Slide 17: How to scan and reconstruct a surface
Data and noise
Noise source
  Outliers from env
  Yumi position
  Laser angle/ range optimal
  3D printing
  Scanning interpolation
  Surface reconstruction

## Slide 18: How to scan and reconstruct a surface
Scanning protocol approach
Scanning time

## Slide 19: Evaluation
End-effector
Laser
Yumi
  Yumi Prototype not exactly calibrated
Scanning protocol
  0 laser angle 20 spline 18deg , (time)
  10 laser angle 20 spline 18 deg , (time)
  0 laser angle 4 spline 90 deg ( time)
  10 laser angle 4 spline 90 deg (time)
  Second approach
Surface Reconstruction
  Different protocol plot ( time)

## Slide 20: Results
Yumi Prototype not exactly calibrated